## Slide 1: Hardware Security
Learning Objectives
  Be able to describe foundational security concepts and secure design principals as it applies to hardware components.
  Be able to describe hardware vulnerabilities and typical defenses.

## Slide 2: Hardware Attacks
Non Invasive attacks
do not harm the device or alter the signals being emitted,
thus making them very hard to detect.
Often called covert channels attacks
  data leakage attacks
  involve closely observing a device’s emissions to gain access to unauthorized data.
Invasive Attacks
involve direct electrical access to the internal components of the device.
E.g. attacker drills a hole into the device place a probe on a bus line to capture a signal.
  During computation of Cryptographic algorithms, known that an attacker who can monitor any bit plane can recover the key.

## Slide 3: Who are potential attackers?
List is wide and varies depending on the type of device.
  technical staff working on a high security machine
  individuals looking to reverse engineer pay-TV smartcards-
  unlocking a mobile phone to use on any network
  mafia looking to build and deploy key-stealing terminals from credit cards.

## Slide 4: Non-invasive attacks
Wiretapping
  Attack:
    Given physical access to cables of a network, especially inexpensive coaxial copper cables, attackers can see all data being transmitted.
  Defenses:
    Use expensive fiber optic cables which transmit light rather than electrical impulses
      More expensive and easier to detect.
    To fully protect data use data encryption, a software solution.
Optimal Emission
  Attack:
    A photo-sensor placed in the room with the CRT display can be trained to reconstruct an image from a screen. The sensor can be 50 meters away.
  Defense:
    use LCD monitors.

## Slide 5: Non-invasive Attacks
Acoustic Emissions
  Attack
    use audio recording of users typing of a keyboard to reconstruct what was typed or recoding a computer to reconstruct CPU instructions.
  Defenses:
    requires training algorithm, thought to be hard to carry out
Power/Timing Emissions
  Attack
    use the fact that different instructions consume different amounts of power or time.
    By measuring the power/time that a device consumes attackers are able to deduce the value of cryptographic keys.
  Defense:
    Do random computations to throw statistics off

## Slide 6: Hardware Defenses
Protections from non-invasive attacks include:
  Emanation Blockage – (prevent)
    build hardware out of materials that block emanation of various signals.
    Examples:
      fiber optic cables for networks,
      screen shields to block visibility
      faraday cages to block electromagnetic emanations in the air.
  Emanation Masking – (prevent)
    inject noise (e.g. a no-op instruction at random in the instruction stream).
    This makes it harder for attackers to analyze the data and pick out patterns.

## Slide 7: Hardware Defenses
Protections from invasive attacks include:
  High end crypto-processors [defensive/deter]
    tamper-sensing membranes
    designed to zero out data, erase memory or self-destruct on tampering.

## Slide 8: Hardware Defenses
General Principal: Minimizing the trusted computing base.
  Crypto-processors
    dedicated processor to perform a predefined set of cryptographic operations which are embedded within a conventional system.
    usually placed in physically tamper-resistant eliminating the need to protect the rest of the sub-system with physical security measures.