## Slide 1: Introduction to Computer Networks
A brief history
Network models
The edge of a network
The core of a network
Network protocols
Network security
Why is network security so bad?

## Slide 2: A Brief History of Computer Networks
1950’s Mainframe with dumb terminals
1960’s Research on packet switching
  ARPAnet (Advanced Research Projects Agency), Internet came from ARPAnet
1970’s Proprietary networks
  ALOHAnet (microwave), Telnet (Britain), Cyclades (France), time-sharing networks (Tymnet, GE), IBM’s SNA
  More research on open networking (ARPAnet  Internet)
1980’s PC, LAN, WAN
  Official deployment of TCP/IP (1983), Minitel project (France), lots of PC/LAN competitors (e.g., Novel netware, IBM token ring)
1990’s Internet explosion
  Tim Berners-Lee created first versions of HTTP, HTML, web server, & web browser (1989-1991)

## Slide 3: What is a network? (A computer engineer’s perspective)
A collection of hardware devices, connected via communication links, that use protocols to transmit data to each other
  Sample hardware devices
    Host (i.e., client, end system), server, packet switch, modem, router
  Sample types of communication links
    Coaxial cable, copper wire, fiber optics, radio spectrum
  Sample (mostly software) protocols
    Ethernet, HTTP, FTP, SMTP, TCP, UDP, IP

## Slide 4: What is a network? (A service-oriented perspective)
A collection of hardware and software components that provide services
  Sample services
    Distributed applications that exchange data
      e.g., web browsing, e-mail, instant messaging, audio/video streaming, telephony, games, peer-to-peer file sharing, remote login
    Connection-oriented reliable service
      Guarantees delivery of data (e.g., landline phone service)
    Connectionless unreliable service
      No guarantee that data is delivered

## Slide 5: What is a network? (A network model perspective)
A layered architecture of hardware and software components
  Sample layered architectures
    Open Systems Interconnection (OSI) Model
      An international standard (ISO/IEC 7498-1)
    Internet Protocol Stack
      Internet Engineering Task Force (IETF)

## Slide 6: Network Models
OSI Model
  A conceptual model
    Describes abstraction layers for a computer network
    Published in 1984
  Consists of 7 layers:
    Application layer
    Presentation layer
    Session layer
    Transport layer
    Network layer
    Data Link layer
    Physical layer
  Wikipedia description
Internet Protocol Stack
  The design of the Internet
    Describes how Internet devices communicate
    Internet activated in 1983
  Consists of 5 layers:
    Application layer
    Transport layer
    Network layer
    Link layer
    Physical layer
  Wikipedia description

## Slide 7: Internet Protocol Stack (Sample Protocols)
Sample application-layer protocols
  HTTP Hyper Text Transfer Protocol
  FTP File Transfer Protocol
  SMTP Simple Mail Transfer Protocol
Sample transport-layer protocols
  TCP Transmission Control Protocol (connection-oriented)
  UDP User Datagram Protocol (connectionless)
Sample network-layer protocols
  IP Internet Protocol
Sample link-layer protocols
  Ethernet
  PPP Point-to-Point Protocol

## Slide 8: Internet Protocol Stack (Terminology)
Basic responsibility of each layer
  Physical
    Communication link or transmission media
  Link
    Uses comm. link to send a frame of bits; basic error detection
  Network
    Routes packets from source to destination
  Transport
    Connection-oriented reliable service
    Connectionless unreliable service
  Application
    Domain-specific message

## Slide 9: The Edge of a Network
End systems
  Computing devices that sit at the edge of a network
    Clients
      e.g., desktop computers, laptop computers, mobile devices, household appliances
    Servers
      e.g., web server, email server, database server
  aka: hosts
    Since an end system runs (hosts) an application program
    Client program
      Designed to request and receive a service from a server
    Server program
      Designed to provide a service to a client

## Slide 10: The Core of a Network
Computing devices that make up the
internals of a network
  Packet switches
    Devices that forward packets closer to their destination
    Communication links connect packet switches together to form various paths between end systems
    Two common types of packet switches
      Routers
      Link layer switches

## Slide 11: The Core of a Network (cont’d)
Computing devices that make up the
internals of a network
  Packet switches (cont’d)
    These devices support two types of communication between applications
    Circuit switching
      A connection-oriented service e.g., analog telephone networks
      Reserves a path between end systems
        buffers, link transmission rate
    Packet switching
      A connectionless service e.g., the Internet
      Each packet sent between end systems may take a different path

## Slide 12: Network Edge, Core and the Internet Protocol Stack
Source
  App sends message M (message)
  Transport layer adds header Ht (segment)
  Network layer adds header Hn (packet)
  Link layer adds header Hl (frame)
  Physical sends bits
Link-layer switch
  Physical receives bits
  Link layer removes Hl
  Link layer adds header Hl
  Physical sends bits
Router
  Physical receives bits
  Link layer removes Hl
  Network layer removes Hn
  Network layer adds Hn
  Link layer adds header Hl
  Physical sends bits
Destination
  Physical receives bits
  Link layer removes Hl (frame)
  Network layer removes Hn (packet)
  Transport layer removes Ht (segment)
  App receives message M (message)

## Slide 13: Network Security
Layers: | Application | Transport | Network | Link | Physical
Confidentiality | MiDC | No | No | No | No
Integrity | MiDC | No | No | No | No
Availability | Maybe | Maybe | No | No | No
Non-repudiation | MiDC | No | No | No | No
Assurance | MiDC | No | No | No | No
Authenticity | MiDC | No | No | No | No
Anonymity | Maybe | Yes | Yes | Yes | Yes
MiDC – Mostly, if Designed Correctly!

## Slide 14: Network Security (Explanations)
Application Layer
MiDC
  Mostly, if Designed Correctly
  Layer can address most concerns associated with goal
May improve availability if:
  It can quickly throw away messages that are invalid (for any reason)
  However, if a DDOS attack has enough machines all sending invalid messages to service it is likely that service will not be able to keep up
May promote anonymity if:
  This is designed into protocol
Transport Layer
May improve availability when:
  TCP is used since TCP includes flow control and congestion control
  These two features allow sending-side of a TCP connection to slow down while waiting for receiving-side to catch up
  This may help, but the physical, link and network layers are still (probably) being overwhelmed

## Slide 15: Network Security (Goals)
Goals (CIA)
  Confidentiality
    Avoiding unauthorized disclosure of information
  Integrity
    Information has been altered only in authorized way
  Availability
    Information is accessible and modifiable in a timely fashion by authorized entities

## Slide 16: Network Security (Fundamental Concepts)
Fundamental Concepts
  Assurance
    How trust is provided and managed in computer systems
    Trust involves interaction of:
      Policies (i.e., behavioral expectations)
      Permissions (i.e., behaviors allowed by agents)
      Protections (i.e., mechanisms that enforce policies and permissions)
  Authenticity
    Ability to determine that statements, policies, and permissions issued by persons or systems are genuine
  Anonymity
    A property that certain records or transactions are not attributable to any individual
  Non-repudiation
    User responsible for their actions and should not be able to deny what they have done

## Slide 17: Why is network security so bad? (History revisited)
1960’s & 70’s
  ARPAnet research leads to Internet
1983
  Official deployment of TCP/IP (1983)
Nov. 2, 1988
  Morris worm (first attack widely discussed in mass media)
1989-1991
  First versions of HTTP, HTML, web server, & web browser
1990’s to today
  Internet growth is exponential
  Number of cyber-attacks and their complexity is increasing
Initial Internet design
  Assumption of trust
    First users were military labs and academic researchers
Early days of Internet
  Lack of malicious behavior
By time Internet exploded
  Too late to change protocols
  Security professionals have been playing catch-up ever since!