## Slide 1: Internet Protocol Stack Network Layer: Security
Security
  Secure protocols
    IP, IPX and VINES provide no security precautions
    IPv6
      Complete redesign of IP, supports authentication and data encapsulation via encryption
    IPsec
      Provides extensions to IP to address security
  Network incompatibility
    Protocols operate in a particular layer, but most protocols still rely on features of a protocol at a higher or lower layer
      Makes it more difficult to change a protocol at a specific layer
  Server filtering
    Filter network traffic coming in to a server
      Attacker must know a valid address in order to gain access
  Firewalls and egress filtering
    Routers can include firewalls to restrict incoming and outgoing packets to specific IP addresses and subnets

## Slide 2: Internet Protocol Network Layer: Routing Risks
Routing Risks
  Direct router attacks
    A DoS or system compromise
      Prevents router from performing basic routing function
  Router table poisoning
    Forged or compromised network traffic can overwrite, insert, or remove valid routing table entries
  Router table flooding
    Router table size is limited (router’s hard drive/RAM not very large)
    Attacker generates fake data to populate router table
    When router tables fills, router can:
      Ignore new routes, discard routes not used, or discard less desirable routes

## Slide 3: Internet Protocol Network Layer: Routing Risks cont’d
Routing Risks (cont’d)
  Routing metric attacks
    Applicable when router uses dynamic metrics
      Attacker forges quality-of-service packets that modify dynamic metrics
      May cause slower throughput, longer paths, more expensive networking costs, disabling a desirable path
  Router looping attacks
    Hard for attacker to accomplish
    A router interface is setup to send packets back to the same router

## Slide 4: Internet Protocol Stack Network Layer: Addressing Risks
Addressing Risks
  Address impersonation
    Two nodes have same address
      i.e., an unplanned impersonation
  Address hijacking
    Two nodes on same subnet have same address
      Node that responds quicker can maintain a network connection
  Dynamic allocation consumption
    Affects addressing schemes that support dynamic addressing
      e.g,. VINES, IPv4, IPv6 with DHCP
    Attack requests all available addresses to be marked as allocated

## Slide 5: Internet Protocol Stack Network Layer: Addressing Risks cont’d
Addressing Risks (cont’d)
  False release attacks
    Attacker impersonates an allocated address and specifies release of the address
    Victim node begins to operate with an unallocated address
      Victim node now vulnerable to impersonation attacks
  False dynamic allocation
    Attacker configures their own allocation server
    Any broadcast request for allocation may be responded by attacker’s allocation server